## Slide 1
Case :
“ Queue Design for Sequencing
- Considering Queue Downtime”
TTMS Proposal Solution Workshop
by
Ramaswamy, Prabhu – Architect, Technology Consulting Group

## Slide 2
Single Queue for all message category
Rabbit MQ with Fail Over Cluster ( Master – Slave ) Hierarchy
HornetQ with Fail Over Cluster
Multiple Queues with Store & Process Mechanism
Multiple Queues , Halt & Proceed
Solution Probabilities
 | Performance | Memory Efficiency | Reliability | Time to Market | Configuration
Single Consolidated Queue |  |  |  |  | 
Rabbit MQ Fail over Clusters |  |  |  |  | 
HornetQ with Fail over Clusters |  |  |  |  | 
Store & Process Mechanism |  |  |  |  | 
Multiple Queue Halt & Proceed |  |  |  |  | 
Comparative Matrix
TTMS Proposal Solution Workshop

## Slide 3
Approach #1 - Single Queue for All Message Category
Technology Pieces: JMS, Boss Hornet MQ
ICE Layer will define separate queues for each message category
On Receiving messages all the queues will post their message in the queue configured in TTMS
TTMS Listener registered will be activated to process messages one by one from the queue.
Separate Error queue will be configured to store the incoming message upon exception
Pros:
Reliable, as no message will be processed in uneven order hence sequence will be maintained
Message sequencing will be taken care automatically hence message posting will be in sequence
Cons:
Processing will be delayed a bit hence the queue length will be more hence everything is pumped in one queue
TTMS Proposal Solution Workshop

## Slide 4
Approach #2 – Rabbit MQ with Fail Over Cluster ( Master – Slave ) Hierarchy
Technology Pieces: Rabbit MQ, Erland
1. Separate queues will be configured in the ICE end to received the message from external system
2. Jboss cluster nodes will be equipped with RabbitMQ & Erlang
3. TTMS Solution will connect with Rabbit MQ and associated listener will be activated to read & process message
4. Separate Error queue will be configured to store the incoming message upon exception
Pros:
Provide failover capability hence ensures high availability ( Messages will be replicated across fail over queues )
Hence independent messages are processed separately it will ensure high performance
Message usage will be distributed hence will avoid memory leaks at peak load scenarios.
Rabbit MQ is implemented based on the ideology of AMQP message distribution centre
No Sequencing will be required hence there wont be any downtime.
Cons:
May see additional permission requirements to install required software in cluster nodes.
Implementation is little difficult comparing other scenarios
Re-configuration may be needed when configuring cluster nodes with direct IP addresses
TTMS Proposal Solution Workshop

## Slide 5
TTMS Proposal Solution Workshop
Approach #3 – HornetQ with Fail Over Cluster
Technology Pieces: JMS, Boss Hornet MQ
1. Separate queues will be configured in the ICE end to received the message from external system
2. Jboss cluster nodes will be configured with Failover queues on HornetQ
3. TTMS Solution will connect with Hornet MQ and associated listener will be activated to read & process message
4. Separate Error queue will be configured to store the incoming message upon exception
Pros:
Provide failover capability hence ensures high availability ( Messages will be replicated across fail over queues )
Hence independent messages are processed separately it will ensure high performance
Message usage will be distributed hence will avoid memory leaks at peak load scenarios.
Configuration is easier hence HornetQ is the jBOSS native implementation
No Sequencing will be required hence there wont be any downtime.
Cons:
May see additional permission requirements to install required software in cluster nodes.
Implementation is little difficult comparing other scenarios

## Slide 6
TTMS Proposal Solution Workshop
Approach #4 – Multiple Queues with Store & Process Mechanism
Technology Pieces: HornetQ, DB2 Neon Drivers, Redwood Schedulers, Java Middleware
1. Separate queues will be configured in the ICE end to received the message from external system
2. Jboss cluster nodes configured with Queue Listener will store the messages to the DB as they receive
3. Frequent batch will be executed to qualify the record to process based on the availability of its parent message
4. Back end trigger will be executed to fetch & store the message to the appropriate tables.
5. Separate Error queue will be configured to store the incoming message upon exception
Pros:
No specific configurations are required and the solution is simple & straightforward
Reliable Solution hence build on top of regular frameworks
Process could take records from the backend for processing through triggers and update the appropriate tables
Sequencing will be maintained through logical order of records in database
Cons:
Won’t provide appreciatable level performance hence multiple processing cycles are involved to validate the message
Latency will be there hence messages won’t be processed as early as they arrived
Complex logic is involved in setting up the record status before and after processing finally

## Slide 7
TTMS Proposal Solution Workshop
Approach #5 – Multiple Queues, Halt & Proceed ( All or None )
Technology Pieces: HornetQ, jBOSS CLI
1. Separate queues will be configured in the ICE end to received the message from external system
2. Jboss cluster nodes will be configured with the listener to process the messages
3. Scheduled batch process will be written to poll the status of queue using CLI Interface
4. If any one queue is down then the listener will be put in halt and will be activated once queue(s) are up
5. Separate Error queue will be configured to store the incoming message upon exception
Pros:
Ensures near real time availability of queues with minimal data errors
No need to sequencing hence failure of one queue will halt others as well to prevent to listen improper messages
Cons:
Hence it puts other queues as well as on hold, it may introduce heavy volume to the process once everything is up
Monitoring interval of the batch may introduce stale messages in the database

## Slide 8
Reference
http://blog.x-aeon.com/2013/04/10/a-quick-message-queue-benchmark-activemq-rabbitmq-hornetq-qpid-apollo/
https://access.redhat.com/documentation/en-US/JBoss_Enterprise_Application_Platform/6.1/html/Administration_and_Configuration_Guide/Configuring_the_HornetQ_Servers_for_Replication.html
https://www.rabbitmq.com/ha.html
Final Recommendation(s)
Contents Consolidated & Rendered by Ramaswamy, Prabhu – Technology Consulting Group
TTMS Proposal Solution Workshop
Solution | Encouraging factors
Hornet Q with Failover Cluster | Reliable hence it is the native jboss implementation Will match nearer availability expectations as of Rabbit MQ Ensures higher degree of performance due to multiple queues/listeners
Single Consolidated Queue | Simple Solution with less time to market Easy Configuration and could leverage server’s JMS capability
Rabbit MQ with Master Slave Dependency | Proven Framework to handle high volume message load Ensures higher degree of performance due to multiple queues/listeners

## Slide 9
TTMS Proposal Solution Workshop
Discussions …